## Slide 1
School of Basic and Applied Sciences
Course Code : BBS01T1002 Course Name: Semiconductor Physics
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
  Effective Mass and Concept of Holes

## Slide 2
Topics to be covered
:
Name of the Faculty: Dr. Aakash Mathur
  Preliminary ideas of E-K diagram
  Introduction
  Derivation of Effective Mass
  Concept of Holes
  References

## Slide 3
Objectives
    Derive and apply concept of Effective Mass
    Explain concept of holes

## Slide 4
Prerequisite/Recapitulations
:
Name of the Faculty: Dr. Aakash Mathur
In a periodic potential lattice, the electron energy values are discontinuous, separated into allowed and forbidden zones occurring alternatively.
The width of the forbidden band increases with E.
As P decreases, the perturbations of the potential due to periodicity of the lattice vanish, making electrons really free, the discontinuous E-K graph will reduce to a continuous parabolic graph as shown by dotted lines and the forbidden bands disappear which is appropriate to the completely free particle. The dotted curve shows the parabola of free electron i.e.,
E=

## Slide 5
Introduction
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
A free electron has well defined mass and obeys Newton’s law when accelerated by an external electric field; but when electron is in periodic potential of the crystal lattice, its behaviour in external electric field is different from that of a free electron. The deviation of the actual electron behaviour than free electron behaviour may be accounted simply by considering the electron to have effective mass, m* rather than free electron mass m.

## Slide 6
Effective Mass
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
.
According to wave mechanical theory (de-Broglie) an electron with velocity v is equivalent to a wave packet moving with group velocity vg
where ω is the angular frequency of de-Broglie wave and K = 2π/λ is propagation constant.
The energy of particle
Now equation (1) gives
........................................................ (2)
............................(1)

## Slide 7
Effective Mass
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
.
For free particle,
Then, from Eqn (2)
This gives linear variation of v with K.
But according to band theory (with periodic potential) of electron, E is not, in general, proportional to K2, there the variation of E with K is as shown in Fig.(a). Using this type of variation of E with K and using equation (2), one can calculate the velocity v, this gives a curve of the type illustrated as in Fig (b). We observe that the velocity of the electron varies with the slope.

## Slide 8
Effective Mass
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
For K=0 and K= ± /a, the slope, dE/dK is zero, thus the velocity of the electron is zero at bottom as well as the top of the first Brillouin Zone.
After K=0, as the value of K increases (i.e., the energy E increases), the velocity increases reaching its maximum value at K=K0 where K0 corresponds to the point of inflection on the E-K graph. Beyond this point the velocity begins to decrease and finally assumes the zero value at K=/a which is the top of the band.
It is significant to note that the decrease of the velocity beyond this point of inflection (with increase in energy) and its zero value at the top of the band are the entirely new features which do not appear at all in the behaviour of free electron.

## Slide 9
Effective Mass
.
Acceleration and effective mass of electron:
When an electron has a well defined mass and accelerated by an electric field, it obeys Newtonian mechanics. Now, we will discuss the behaviour of electron when it is to be accelerated inside a crystal due to external electric field.
When an electric field
is applied on the electron, then force on electron
Work done by electric field over a small distance dx travelled in time dt is
dE= -eXe dx = -eXe v dt
Substituting value of v from equation (2), we get
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 10
Effective Mass
Acceleration and effective mass of electron:
Differentiating eqn (2) with respect to time
, --------(4)
When we compare this result with the acceleration of a free electron of mass m i.e.
---------(5)
Compare eqn. (4) and (5) it follows that an electron in the periodic lattice behaves as an electron of effective mass m* given by
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 11
Effective Mass
Acceleration and effective mass of electron:
Clearly the effective mass of electron is determined by d2E/dK2 and is a function of K is no longer a strict constant.
It indicates the importance of E-K curves for the motion of electron. [(Fig (c)] represents the effective mass (m*) of the electron as a function of K.
It increases with increase of K, becomes maximum at point of inflexion and then it becomes negative. The behaviour of the effective mass is as follows
It increases with increase of K, becomes maximum at point of inflexion and then it becomes negative.
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 12
Effective Mass
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 13
Concept of Holes
The behaviour of the effective mass is as follows
m* is positive in the lower half of the energy band
m* is negative in the upper half of the energy band.
Physically it means since this region is now close to the top of the band that in upper half of the band, electron behaves as a positively charged particle. The negative mass can be seen dynamically by noting that the velocity decreases, thus acceleration negative i.e., opposite to the applied force, implying a negative mass. This means that in this region the lattice exerts such a large retarding force on the electron that it overcomes the applied force and produces a negative acceleration. Here the band behaves as a positively charged particle referred to as a hole.
At inflexion points (K=K0) in E-K curves, the effective mass m* becomes infinite.
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 14
Concept of Holes
For a free electron,
But for a periodic potential, m*  m
It may be concluded that all the results of the free electron are correct provided m in each case is replaced by suitable m*. Accordingly energy in periodic potential will be given by
This is known as the effective mass approximation.
As a summary, in the periodic potential, the electron in the crystal will thus behave dynamically just like a particle with variable effective mass and the whole effect of the periodic potential on the motion of the electron is to replace the free electron mass with proper effective mass.
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech

## Slide 15
Degrees of Freedom
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
The degree of freedom of an electron in periodic potential is defined by a factor
fK is a measure of the extent to which an electron in state K is free.
If m* is large, i.e. the electron behaves as a heavy particle. When fk = 1, the electron behaves as free particle, Fig. (d) represents the plot of fK against K. It may be noted that fK is positive in the lower half of the band and negative in upper half.

## Slide 16
Practice Questions
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
Draw and explain E-K diagram.
2. Draw and explain Brillouin zones in one dimension

## Slide 17
School of Basic and Applied Sciences
Course Code : BBS01T1002 Course Name: Semiconductor Physics
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
1. J. Singh , Semiconductor optoelectronics, Physics and Technology, Mc-Graw –Hill Inc. 1995.
2. S.M. Sze, Semiconductor Devices: Physics and Technology, Wiley 2008.
3. Pillai S O, Solid State Physics,( 2010), sixth edition, New Age International (P) Ltd. ISBN-9788122427264.
References

## Slide 18
School of Basic and Applied Sciences
Course Code : BBS01T1002 Course Name: Semiconductor Physics
Name of the Faculty: Dr. Aakash Mathur Program Name: B.Tech
Thank you